## Slide 1
CUMBERLAND COUNTY
SCICNet
Motorola APX
Mobile Radio
E5 Control Head
Notes: Learning Event Description:
This learning event provides subscriber unit users an introduction to their unit, its basic operation, and the job aids available for assistance in operation. This is accomplished through the use of video clips, instructor facilitation, and hands-on activities whereby users are able to perform common tasks associated with unit operation.
Learning Event Objective:
Upon completion, the participant should be able to employ the toolkit resource needed to accomplish an operational task.
Learning Event Description:
This learning event provides subscriber unit users an introduction to their unit, its basic operation, and the job aids available for assistance in operation. This is accomplished through the use of video clips, instructor facilitation, and hands-on activities whereby users are able to perform common tasks associated with unit operation.
Learning Event Objective:
Upon completion, the participant should be able to employ the toolkit resource needed to accomplish an operational task.

## Slide 2: Copyrights / Disclaimer
Computer Software Copyrights The Motorola products described in this manual may include copyrighted Motorola computer programs stored in semiconductor memories or other media. Laws in the United States and other countries preserve for Motorola certain exclusive rights for copyrighted computer programs, including, but not limited to, the exclusive right to copy or reproduce in any form the copyrighted computer program. Accordingly, any copyrighted Motorola computer programs contained in the Motorola products described in this manual may not be copied, reproduced, modified, reverse-engineered, or distributed in any manner without the express written permission of Motorola. Furthermore, the purchase of Motorola products shall not be deemed to grant either directly or by implication, estoppel, or otherwise, any license under the copyrights, patents or patent applications of Motorola, except for the normal non-exclusive license to use that arises by operation of law in the sale of a product. | Documentation Copyrights No duplication or distribution of this document or any portion thereof shall take place without the express written permission of Motorola. No part of this manual may be reproduced, distributed, or transmitted in any form or by any means, electronic or mechanical, for any purpose without the express written permission of Motorola. Disclaimer The information in this document is carefully examined, and is believed to be entirely reliable. However no responsibility is assumed for inaccuracies. Furthermore, Motorola reserves the right to make changes to any products herein to improve readability, function, or design. Motorola does not assume any liability arising out of the applications or use of any product or circuit described herein; nor does it cover any license under its patent rights nor the rights of others.
APX Mobile Radio
E5 Control Head

## Slide 3: Welcome
This tutorial has been prepared exclusively for you, based on your system configuration and radio layout.
It has been designed for easy comprehension, and guides you through each procedure, step by step. However, for in-depth system or radio information, you should consult your system administrator.
Keep in mind that each radio and each system is customer configurable.
APX Mobile Radio
E5 Control Head
Notes: WELCOME participants to the learning event and introduce yourself.
TELL participants that this learning event takes approximately 2 to 3 hours to complete.
TELL participants that this event consists of interactive tutorials, video clips and hands-on activities.
STATE the Learning Objective for the course.
Learning Event Objective:
Upon completion of the learning event, the participant should be able to employ the toolkit resource needed to accomplish a task.

## Slide 4: Radio Overview
Dimmer
Button
Home
Button
Volume
Knob
Emergency
Button
Mode
Knob
Soft Menu
Keys
Power
Button
4-Way Navigation
Buttons
E5 Programmable
Button (not used)
APX Mobile Radio
E5 Control Head

## Slide 5: Display
APX Mobile Radio
E5 Control Head
APX Mobile Radio
E5 Control Head
E5 Control Head Display:
The E5 control head uses LED indicator lights and icons

## Slide 6: Display Indicators
APX Mobile Radio
E5 Control Head
APX Mobile Radio
E5 Control Head

## Slide 7: Display Indicators – cont’d.
APX Mobile Radio
E5 Control Head
APX Mobile Radio
E5 Control Head

## Slide 8: Status Alert Tones
Tone Name |  | Tone Information
Acknowledge |  | A call or emergency sent to the central controller has been acknowledged
Button Press |  | A valid key was pressed on the keypad
Call Alert |  | Call Alert page received by your radio
Emergency |  | Emergency alarm was sent from your radio and acknowledged
Out of Range |  | Radio is out of range of the system (trunking only)
Power-up |  | Radio has successfully powered on
Prohibit |  | Radio is unable to access the system or selected talkgroup
System Busy |  | Channel, system or target radio is busy
Talk Permit |  | Channel is ready to use
Time-out Timer |  | Time-out timer limit has been reached
APX Mobile Radio
E5 Control Head
Notes: Pressing the speaker icon in the presentation mode will play the sound as defined in the “Tone Information”area.

## Slide 9: LED Status
Solid
Conventional channel is busy
Blinking
Radio is receiving a secured transmission
YELLOW
Solid
Radio is transmitting
Double-Blinking
Radio is transmitting and emergency call
RED
Solid
Self-test being performed
Blinking
Radio is on a priority channel while in Scan List Programming mode
GREEN
MS01
MS02
MS03
SCAN
NUIS
CUMBERLAND
COUNTY
APX Mobile Radio
E5 Control Head
Notes: Describe the LED status, Red VS Amber and solid VS flashing.

## Slide 10: Radio Features & Menu Items
APX Mobile Radio
E5 Control Head
General Radio Features
and
Menu Item Functions

## Slide 11: Radio On or Off
Your Mobile Radio is likely wired to power on and off with your vehicle, either by ignition-sense or when the apparatus’ batteries are turned on.
Note that turning the radio manually on/off may desynchronize its ignition-sense, even when wired correctly.
Manually Turn Radio On:
Press the Power button on the control unit.
The radio will perform a self test during power up.
Manually Turn Radio Off:
Press the power button on the control unit.
General Radio Features
Power Button
APX Mobile Radio
E5 Control Head

## Slide 12: Volume Set
Rotate the Volume knob clockwise to increase the volume and counterclockwise to decrease the volume.
To set the volume:
General Radio Features
Volume Knob
APX Mobile Radio
E5 Control Head

## Slide 13: Display Brightness
Press the Dimmer button to change the display brightness.
Pressing and holding this button will toggle the display between day and night mode.
To adjust display brightness:
General Radio Features
Dimmer Button
APX Mobile Radio
E5 Control Head

## Slide 14: Home Mode Select
To select the home mode:
Press and hold .
This will revert the radio to your pre-programmed ‘Home Channel.’ This is set as the primary dispatch talkgroup for your Home County.
General Radio Features
Home Button
APX Mobile Radio
E5 Control Head
Notes: This feature must be enabled by a qualified radio technician.

## Slide 15: Changing Zones or Channels
Mode Name
Zone Name
General Radio Features
Mode Knob
Cmb Zone A
Channel 1
Mode Select Menu Items
The “Mode Select Menu Items” allow users to program any desired zone/channel combination. A long-press will assign the currently selected Zone/Channel; a short-press will revert the radio to the user-defined setting.
“Mode Knob” will scroll through the channel list of the currently selected zone.
The “Up and Down Buttons” on the 4-Way Navigation Buttons will allow users to scroll upwards or downwards through the zone list.
Up and Down Buttons
(4-Way Navigation
Buttons)
APX Mobile Radio
E5 Control Head
Notes: Explain the difference between Mode and Zone

## Slide 16: Scan On/Off and Nuisance Delete
To Temporarily Delete a Nuisance Mode:
Note:
The Selected Channel and Primary Dispatch cannot be Nuisance Deleted
Press the menu button below “NUIS” while actively scanning the talkgroup you wish to temporarily delete to no longer hear traffic from a busy talkgroup in the scan list. To restore the original scan list, do one of the following: Turn scan off, then on. Change modes. Turn off the radio, and then turn it back on.
General Radio Features
Cmb Zone A
Channel 1
To Turn Scan On or Off:
Press the menu button below “SCAN.” When scan is being enabled, the icon will appear at the top of the radio’s display. Likewise, when scan is turned off this icon will disappear.
APX Mobile Radio
E5 Control Head

## Slide 17: Scan List Programming Mode
To Edit The Scan List:
Use Left or Right on the 4-Way Navigation Buttons to toggle the displayed Menu Items. Select ‘SCNL’ to enter Scan List Programming Mode.
General Radio Features
Cmb Zone A
Channel 1
Left and Right Buttons
(4-Way Navigation
Buttons)
SCNL
REKY
RSSI
APX Mobile Radio
E5 Control Head

## Slide 18: Scan List Programming Mode
Pressing ‘SEL’ will add the currently displayed channel to the scan list.
General Radio Features
Cmb Zone A
Channel 1
SEL
DEL
RCL
APX Mobile Radio
E5 Control Head
Select ‘DEL’ to remove the currently displayed channel from the scan list. An item deleted from the scan list will not be scanned until added back in manually.
Selecting ‘RCL’ will toggle through all resources currently assigned to the scan list. These can be as you
A short press of the Home Button will Exit the Scan List Programming mode
Notes:
Primary Dispatch cannot be Deleted from the scan list.
If a scan list is full, you will hear a bad-key chirp each time you press “SEL,” and the desired channel will not be assigned to the list. A Scan List will hold a maximum 15 talkgroups or channels.
Conventional Channels and Trunking Talkgroups cannot be scanned simultaneously.

## Slide 19: Transmit (Trunked Modes)
Lift the microphone off-hook. Press and hold the microphone PTT button.
If you hear three quick tones (callback tones) and the red XMIT (transmit) indicator lights steadily, proceed with your message.
  If you hear a busy tone and the yellow Busy indicator flashes, all trunked channels are in use.
  Release the PTT button and wait for the three quick tones. Within three seconds of hearing these tones, press and hold the PTT button to transmit your message.
  If you hear a continuous low-pitched tone, you are out of the system's range. The red XMIT indicator may flash several times as the radio tries to access the system.
Release the PTT button to receive.
Trunked Radio Features
Cmb Zone A
Channel 1
APX Mobile Radio
E5 Control Head
PTT Button on Mobile Mic

## Slide 20: Over-The-Air Rekeying (Encrypted Radios Only)
It may occasionally be necessary for users to initiate an Over-The-Air Rekey (OTAR) Request. To do so:
Verify the IP Icon is displayed
Press the “REKY” menu button
“REQUEST REKEY” will appear on the display
Press the PTT
The display will indicate “PLEASE WAIT”
A chirp will be heard upon a successful rekey
General Radio Features
Trunked Radio Features
Cmb Zone A
Channel 1
SCNL
REKY
RSSI
APX Mobile Radio
E5 Control Head
Note:
Contact your System Administrator promptly if an encryption-capable radio is unable to successfully perform an Over-The-Air Rekey for any reason.

## Slide 21: Encrypted Communications Overview
The Motorola Solutions ASTRO® 25 secure communication solution allows two-way voice and data transmissions to be secured using an “encryption key.” An encryption key is a sequence of characters used to encode and protect voice and data traffic from being intercepted by unauthorized devices and individuals.
Only devices configured with a matching encryption key can properly decode received voice and data traffic.
General Radio Features
Trunked Radio Features
APX Mobile Radio
E5 Control Head
Note:
The icon indicates that a selected mode is an encrypted talkgroup or channel.

## Slide 22: Encrypted Communications Overview (cont’d)
If a device does not support encryption, it cannot function on an encrypted talkgroup or channel. This means that non-encrypted and encrypted devices are only interchangeable between departments or agencies that either do or do not utilize encryption in their modes of communication.
Consult your System Administrator for more information.
General Radio Features
Trunked Radio Features
Cmb Zone A
Channel 1
SCNL
REKY
RSSI
APX Mobile Radio
E5 Control Head
Note:
The icon indicates that a selected mode is an encrypted talkgroup or channel.

## Slide 23: Received Signal Strengh Indicator
Pressing the “RSSI” menu button will display the Signal Strength to the radio from the nearest tower. This is displayed simultaneously in RSSI and dBm.
General Radio Features
Trunked Radio Features
Cmb Zone A
Channel 1
SCNL
REKY
RSSI
APX Mobile Radio
E5 Control Head

## Slide 24: Emergency Alarm
Press the Emergency button. A tone sounds and the display alternates EMERGENCY with the current zone/mode. For trunking modes, a high-pitched tone indicates that the alarm has been received by the trunked system’s central controller. 2. Radio goes into hot mic for 10 seconds, which means there is no need to press the Push-To-Talk to Transmit during this period of time. After this 10 second time period, the radio remains in emergency but a PTT will be required to relay voice communication.
This feature allows the radio to send an Emergency Beacon, which will be received by Dispatchers and other radios.
Interactive Procedure
Trunked Radio Features
Emergency Button
EMERGENCY
APX Mobile Radio
E5 Control Head
To Initiate Emergency:
Cmb Zone A
Channel 1
SCNL
REKY
RSSI
To Reset the Emergency:
Once a Dispatcher has confirmed emergency has been acknowledged at the Dispatch Console, press and hold the Emergency button for 3 seconds. A long steady tone sounds and EMERGENCY will no longer be indicated in display.
Notes: For trunking modes, a high-pitched tone sounds indicating that the alarm has been received by the trunked central controller.

## Slide 25: Dynamic Regrouping
Trunked Radio Features
Notes:
System Management Function ONLY
Dynamic Regrouping allows the Dispatcher or System Administrator to temporarily reassign selected individuals, operating in separate trunked talkgroups, into a single group so they can communicate.
Being Assigned to a Dynamic Regroup:
Once the Dynamic Regroup has been initiated, navigate to
Press the PTT button to communicate to others in the Dynamic Regroup
Cmb Zone B
Dynam Regroup
MS01
MS02
MS03
SCAN
NUIS
APX Mobile Radio
E5 Control Head
Notes: When you press the PTT button, the radio transmits on the dynamically assigned mode.
After the dispatcher releases your mobile from the dynamic ID assignment, your radio returns to the last selected, non-dynamic regrouping mode.
If no dynamic regrouping assignment has been made, an illegal-mode tone sounds if you attempt to select a dynamic mode. This means that the selection is not valid.

## Slide 26: Site Trunking
Trunked Radio Features
Site Trunking is a unique Trunking mode that is considered to be an interim mode of Wide Trunking.
On a P25 system, if a site should lose all connectivity to the System Core it sends out a message indicating that it is now in “Site Trunking” mode. It will continue to send out this message until link to the Core is repaired. Radios connected to a site in Site Trunking will be able to communicate with each other locally, but calls will not be received by units affiliated at other sites.
MS01
MS02
MS03
SCAN
NUIS
APX Mobile Radio
E5 Control Head
Cmb Zone A
Site Trunking
Notes: When you press the PTT button, the radio transmits on the dynamically assigned mode.
After the dispatcher releases your mobile from the dynamic ID assignment, your radio returns to the last selected, non-dynamic regrouping mode.
If no dynamic regrouping assignment has been made, an illegal-mode tone sounds if you attempt to select a dynamic mode. This means that the selection is not valid.

## Slide 27
MS01
MS02
MS03
SCAN
NUIS
APX Mobile Radio
E5 Control Head
Cmb Zone A
Channel 1
Examples of Agency Fleetmaps:

## Slide 28
APX Mobile Radio
E5 Control Head
EMS Fleetmap

## Slide 29
APX Mobile Radio
E5 Control Head
EMS Fleetmap (cont’d)

## Slide 30
APX Mobile Radio
E5 Control Head
Law Enforcement Fleetmap

## Slide 31
APX Mobile Radio
E5 Control Head
Law Enforcement Fleetmap (cont’d)

## Slide 32
APX Mobile Radio
E5 Control Head
Fire Fleetmap

## Slide 33
APX Mobile Radio
E5 Control Head
Fire Fleetmap (cont’d)

## Slide 34
APX Mobile Radio
E5 Control Head
Fire Police Fleetmap

## Slide 35
APX Mobile Radio
E5 Control Head
Fire Police Fleetmap (cont’d)

## Slide 36: Thank You for Your Participation!
ASTRO®
XTL™ 5000 Digital Mobile Radio
Model O5
Interactive End-User Training
36
:
►
◄
9
►
SCICNet
Motorola APX
Mobile Radio
E5 Control Head