## Slide 1
CUMBERLAND COUNTY
SCICNet
Motorola
APX NEXT
Portable Radio
Notes: Learning Event Description:
This learning event provides subscriber unit users an introduction to their unit, its basic operation, and the job aids available for assistance in operation. This is accomplished through the use of video clips, instructor facilitation, and hands-on activities whereby users are able to perform common tasks associated with unit operation.
Learning Event Objective:
Upon completion, the participant should be able to employ the toolkit resource needed to accomplish an operational task.
Learning Event Description:
This learning event provides subscriber unit users an introduction to their unit, its basic operation, and the job aids available for assistance in operation. This is accomplished through the use of video clips, instructor facilitation, and hands-on activities whereby users are able to perform common tasks associated with unit operation.
Learning Event Objective:
Upon completion, the participant should be able to employ the toolkit resource needed to accomplish an operational task.

## Slide 2: Copyrights / Disclaimer
Computer Software Copyrights The Motorola products described in this manual may include copyrighted Motorola computer programs stored in semiconductor memories or other media. Laws in the United States and other countries preserve for Motorola certain exclusive rights for copyrighted computer programs, including, but not limited to, the exclusive right to copy or reproduce in any form the copyrighted computer program. Accordingly, any copyrighted Motorola computer programs contained in the Motorola products described in this manual may not be copied, reproduced, modified, reverse-engineered, or distributed in any manner without the express written permission of Motorola. Furthermore, the purchase of Motorola products shall not be deemed to grant either directly or by implication, estoppel, or otherwise, any license under the copyrights, patents or patent applications of Motorola, except for the normal non-exclusive license to use that arises by operation of law in the sale of a product. | Documentation Copyrights No duplication or distribution of this document or any portion thereof shall take place without the express written permission of Motorola. No part of this manual may be reproduced, distributed, or transmitted in any form or by any means, electronic or mechanical, for any purpose without the express written permission of Motorola. Disclaimer The information in this document is carefully examined, and is believed to be entirely reliable. However no responsibility is assumed for inaccuracies. Furthermore, Motorola reserves the right to make changes to any products herein to improve readability, function, or design. Motorola does not assume any liability arising out of the applications or use of any product or circuit described herein; nor does it cover any license under its patent rights nor the rights of others.
APX Portable Radios

## Slide 3: Welcome
This tutorial has been prepared exclusively for you, based on your system configuration and radio layout.
It has been designed for easy comprehension, and guides you through each procedure, step by step. However, for in-depth system or radio information, you should consult your system administrator.
Keep in mind that each radio and each system is customer configurable.
APX Portable Radios
Cumberland
County
Cumberland
County
Notes: WELCOME participants to the learning event and introduce yourself.
TELL participants that this learning event takes approximately 2 to 3 hours to complete.
TELL participants that this event consists of interactive tutorials, video clips and hands-on activities.
STATE the Learning Objective for the course.
Learning Event Objective:
Upon completion of the learning event, the participant should be able to employ the toolkit resource needed to accomplish a task.

## Slide 4: Radio Overview
Cumberland
County
Soft Menu
Keys
APX Portable Radios
2-Position
Concentric
Switch
Channel/Mode
Select Knob
Power On/Off
Volume Control
Home
Button
Emergency
Button
3-Position
Switch
Cumberland
County
Zone
Radio 1
Display Sleep/Wake
Push-To-Talk (PTT) Button
Middle Side
Button (1 dot)
Bottom Side
Button (2 dot)
Top Side Button
(purple)
Speaker Grille Button

## Slide 5: Display Indicators
APX Portable Radios

## Slide 6: Display Indicators – cont’d.
APX Portable Radios
Note:
Battery indicator will not appear on Portables if the battery is not properly and regularly conditioned.

## Slide 7: Status Alert Tones
Tone Name |  | Tone Information
Acknowledge |  | A call or emergency sent to the central controller has been acknowledged
Button Press |  | A valid key was pressed on the keypad
Call Alert |  | Call Alert page received by your radio
Emergency |  | Emergency alarm was sent from your radio and acknowledged
Out of Range |  | Radio is out of range of the system (trunking only)
Power-up |  | Radio has successfully powered on
Prohibit |  | Radio is unable to access the system or selected talkgroup
System Busy |  | Channel, system or target radio is busy
Talk Permit |  | Channel is ready to use
Time-out Timer |  | Time-out timer limit has been reached
APX Mobile Radio
E5 Control Head
Notes: Pressing the speaker icon in the presentation mode will play the sound as defined in the “Tone Information”area.

## Slide 8: LED Status
Solid
Conventional channel is busy
Blinking
Radio is receiving a secured transmission
YELLOW
Solid
Radio is transmitting
Double-Blinking
Radio is transmitting and emergency call
RED
Solid
Self-test being performed
Blinking
Radio is on a priority channel while in Scan List Programming mode
GREEN
Cumberland
County
APX Portable Radios
Cumberland
County
Zone
Radio 1
Notes: Describe the LED status, Red VS Amber and solid VS flashing.

## Slide 9: Radio Features & Menu Items
General Radio Features
and
Menu Item Functions
APX Portable Radios
Cumberland
County
Zone
Radio 1

## Slide 10: Radio On or Off
General Radio Features
APX Mobile Radio
E5 Control Head
APX Portable Radios
Cumberland
County
Cumberland
County
Power On/Off
Volume Control
The APX Portable radio is turned on by rotating the Power/Volume Control Knob clockwise. It will click and the radio will begin power up and self-test sequence.
The APX Portable radio is turned off by rotating the Power/Volume Control Knob counter-clockwise until it clicks.
Rotate the Volume knob clockwise to increase the volume and counterclockwise to decrease the volume.
Zone
Radio 1

## Slide 11: Home Mode Select
To select the home mode:
General Radio Features
Home Button
APX Mobile Radio
E5 Control Head
APX Portable Radios
Press and hold .
This will revert the radio to your pre-programmed ‘Home Channel.’ This is set as the primary dispatch talkgroup for your Home County.
Cumberland
County
Zone
Radio 1
Notes: This feature must be enabled by a qualified radio technician.

## Slide 12: Changing Zones or Channels
General Radio Features
APX Mobile Radio
E5 Control Head
APX Portable Radios
Cmb ZoneA
Channel 1
Cmb ZoneA
Channel 1
To select a zone outside of the first three in the fleetmap, select the ‘Zone’ menu button and use the touch display to navigate through the zone list.
Zone Name
3-Position
Switch
C
Zone Menu Item
To toggle between the first three zones of the fleetmap, move the 3-Position Switch to Position A, B, or C to select Zone 1, 2, or 3 of the radio fleetmap.
Cmb ZoneA
Channel 1
Zone
ScnL
Mode Name
Zone
Radio 1

## Slide 13: Changing Zones or Channels
General Radio Features
APX Mobile Radio
E5 Control Head
APX Portable Radios
Cmb ZoneA
Channel 1
Cmb ZoneA
Channel 1
Zone Name
Cmb ZoneA
Channel 1
Zone
ScnL
Mode Name
Channel/Mode
Select Knob
Use the Channel/Mode Select Knob to change the selected mode/channel within the selected zone. The touch display can also be used.
Zone
Radio 1
Note:
Using the touch display to change the selected mode/channel will result in the channel selector being in a different position than what is actually selected on the radio

## Slide 14: Keypad/Control Lock
General Radio Features
APX Mobile Radio
E5 Control Head
APX Portable Radios
2-Position
Concentric Switch
The APX Portable controls can be locked to prevent accidental an accidental button press using the 2-Position Concentric Switch, located beneath the Channel Selector Knob.
- Position the switch on this icon to lock the buttons.
- Position the switch on this icon to unlock the buttons.
Note:
These controls will not be impacted when the Control Lock is enabled:
Volume/Power Knob
Mode Select Knob
3-Position Switch
Emergency Button
PTT Button
Cmb ZoneA
Channel 1

## Slide 15: Transmit (Trunked Modes)
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
PTT Button on Portable RSM
Lift the microphone off-hook. Press and hold the microphone PTT button.
If you hear three quick tones (callback tones) and the red XMIT (transmit) indicator lights steadily, proceed with your message.
  If you hear a busy tone and the yellow Busy indicator flashes, all trunked channels are in use.
  Release the PTT button and wait for the three quick tones. Within three seconds of hearing these tones, press and hold the PTT button to transmit your message.
  If you hear a continuous low-pitched tone, you are out of the system's range. The red XMIT indicator may flash several times as the radio tries to access the system.
Release the PTT button to receive.
Cmb ZoneA
Channel 1
Zone
ScnL
PTT Button on side of Portable radio
Zone
Radio 1

## Slide 16: ViQi Voice Control
General Radio Features
APX Mobile Radio
E5 Control Head
APX Portable Radios
Speaker Grille Button
This button allows access to the ViQi Voice Control feature. To use this feature, press and hold the button while making a voice command. For example: “What is my volume,” or “change volume.”

## Slide 17: Light/Flip
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
A short-press of the Middle Side Button will illuminate the backlight of both the front and top displays on the portable. A long-press of the Middle Side Button will flip the top display’s orientation by 180 degrees.
Cmb ZoneA
Channel 1
Cmb ZoneA
Channel 1

## Slide 18: Scan On/Off and Nuisance Delete
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
To Turn Scan On or Off:
Press the Top Side button. When scan is being enabled, the icon will appear at the top of the radio’s display. Likewise, when scan is turned off this icon will disappear.
To Temporarily Delete a Nuisance Mode:
Note:
The Selected Channel and Primary Dispatch cannot be Nuisance Deleted
Press the Bottom Side button below “NUIS” while actively scanning the talkgroup you wish to temporarily delete to no longer hear traffic from a busy talkgroup in the scan list. To restore the original scan list, do one of the following: Turn scan off, then on. Change modes. Turn off the radio, and then turn it back on.
Cmb ZoneA
Channel 1
ScnL
Zone
Zone
Radio 1

## Slide 19: Scan List Programming Mode
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
To Edit The Scan List:
Select the ‘SCNL’ Menu Item to enter Scan List Programming Mode.
Cmb ZoneA
Channel 1
ScnL
Zone
Zone
Radio 1

## Slide 20: Scan List Programming Mode
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Viewing The Scan List Members:
After selecting the ‘SCNL’ menu item, the current selected items of the scan list will display first.
Cmb ZoneA
Channel 1
ScnL
Zone
Notes:
Primary Dispatch cannot be Deleted from the scan list.
If a scan list is full, you will hear a bad-key chirp each time you press “SEL,” and the desired channel will not be assigned to the list. A Scan List will hold a maximum 15 talkgroups or channels.
Conventional Channels and Trunking Talkgroups cannot be scanned simultaneously.

## Slide 21: Scan List Programming Mode
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Editing The Scan List Members:
Select ‘Channels’ on the touch screen to add channels to the scan list from the currently selected to.
Cmb ZoneA
Channel 1
ScnL
Zone
Notes:
Primary Dispatch cannot be Deleted from the scan list.
If a scan list is full, you will hear a bad-key chirp each time you press “SEL,” and the desired channel will not be assigned to the list. A Scan List will hold a maximum 15 talkgroups or channels.
Conventional Channels and Trunking Talkgroups cannot be scanned simultaneously.

## Slide 22: Scan List Programming Mode
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Editing The Scan List Members:
Select ‘X Scan List’ on the touch screen to Exit the Scan List Programming mode.
Cmb ZoneA
Channel 1
ScnL
Zone
Note:
If a scan list is full, you will hear a bad-key chirp each time you press “SEL,” and the desired channel will not be assigned to the list.
Note:
Primary Dispatch cannot be Deleted from the scan list.

## Slide 23: Other Menu Items
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Select the icon from the display to access additional menu items on the portable: Rekey Request: Allows for a user-initiated Over-The-Air Rekey Request. Bluetooth: Provides a list a Bluetooth status/information and Bluetooth options, such as turning Bluetooth On/Off and view currently active paired or available Bluetooth devices. Profiles: Allows you to select one of the programmed Radio Profiles to adjust mic sensitivity, speaker settings, and backlight settings. WiFi: Allows you to view current WiFi status and settings.
Cmb ZoneA
Channel 1
ScnL
Zone
Zone
Radio 1

## Slide 24: Over-The-Air Rekeying (Encrypted Radios Only)
Trunked Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Note:
Contact your System Administrator promptly if an encryption-capable radio is unable to successfully perform an Over-The-Air Rekey for any reason.
It may occasionally be necessary for users to initiate an Over-The-Air Rekey (OTAR) Request. To do so:
Verify the IP Icon is displayed
Press the “REKY” menu button
“REQUEST REKEY” will appear on the display
Press the PTT
The display will indicate “PLEASE WAIT”
A chirp will be heard upon a successful rekey

## Slide 25: Encrypted Communications Overview
The Motorola Solutions ASTRO® 25 secure communication solution allows two-way voice and data transmissions to be secured using an “encryption key.” An encryption key is a sequence of characters used to encode and protect voice and data traffic from being intercepted by unauthorized devices and individuals.
Only devices configured with a matching encryption key can properly decode received voice and data traffic.
General Radio Features
Trunked Radio Features
APX Portable Radios
Note:
The icon indicates that a selected mode is an encrypted talkgroup or channel.

## Slide 26: Encrypted Communications Overview (cont’d)
General Radio Features
Trunked Radio Features
APX Portable Radios
Note:
The icon indicates that a selected mode is an encrypted talkgroup or channel.
Cmb ZoneA
Channel 1
ScnL
Zone
Zone
Radio 1
If a device does not support encryption, it cannot function on an encrypted talkgroup or channel. This means that non-encrypted and encrypted devices are only interchangeable between departments or agencies that either do or do not utilize encryption in their modes of communication.
Consult your System Administrator for more information.

## Slide 27: Emergency Alarm Activation
Trunked Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
This feature allows the radio to send an Emergency Beacon, which will be received by Dispatchers and other radios.
To Initiate Emergency:
Press the Emergency button. A tone sounds and the display alternates EMERGENCY with the current zone/mode. For trunking modes, a high-pitched tone indicates that the alarm has been received by the trunked system’s central controller. 2. Radio goes into hot mic for 10 seconds, which means there is no need to press the Push-To-Talk to Transmit during this period of time. After this 10 second time period, the radio remains in emergency but a PTT will be required to relay voice communication.
Emergency Button
Cmb ZoneA
Channel 1
ScnL
Zone
Cmb ZoneA
Channel 1
Zone
Radio 1

## Slide 28: Emergency Alarm Reset
Trunked Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
This feature allows the radio to send an Emergency Beacon, which will be received by Dispatchers and other radios.
Emergency Button
Cmb ZoneA
Channel 1
ScnL
Zone
Cmb ZoneA
Channel 1
To Reset the Emergency:
Once a Dispatcher has confirmed emergency has been acknowledged at the Dispatch Console, press and hold the Emergency button for 3 seconds. A long steady tone sounds and EMERGENCY will no longer be indicated in display.
Zone
Radio 1

## Slide 29: Dynamic Regrouping
Trunked Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Notes:
System Management Function ONLY
Dynamic Regrouping allows the Dispatcher or System Administrator to temporarily reassign selected individuals, operating in separate trunked talkgroups, into a single group so they can communicate.
Being Assigned to a Dynamic Regroup:
Once the Dynamic Regroup has been initiated, navigate to
Press the PTT button to communicate to others in the Dynamic Regroup
Cmb ZoneB
Dynam Regroup
ScnL
Zone
Zone
Radio 1

## Slide 30: Site Trunking
Trunked Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Cmb ZoneA
Channel 1
Site Trunking
Zone
Radio 1
Site Trunking is a unique Trunking mode that is considered to be an interim mode of Wide Trunking.
On a P25 system, if a site should lose all connectivity to the System Core it sends out a message indicating that it is now in “Site Trunking” mode. It will continue to send out this message until link to the Core is repaired. Radios connected to a site in Site Trunking will be able to communicate with each other locally, but calls will not be received by units affiliated at other sites.

## Slide 31
Cmb Zone A
Channel 1
APX Portable Radios
Cmb ZoneA
Channel 1
Zone
Radio 1
Examples of Agency Fleetmaps:

## Slide 32
APX Portable Radios
EMS Fleetmap

## Slide 33
APX Portable Radios
EMS Fleetmap (cont’d)

## Slide 34
APX Portable Radios
Law Enforcement Fleetmap

## Slide 35
APX Portable Radios
Law Enforcement Fleetmap (cont’d)

## Slide 36
APX Portable Radios
Fire Fleetmap

## Slide 37
APX Portable Radios
Fire Fleetmap (cont’d)

## Slide 38
APX Portable Radios
Fire Police Fleetmap

## Slide 39
APX Portable Radios
Fire Police Fleetmap (cont’d)

## Slide 40: Thank You for Your Participation!
ASTRO®
XTL™ 5000 Digital Mobile Radio
Model O5
Interactive End-User Training
40
:
►
◄
9
►
SCICNet
Motorola
APX NEXT
Portable Radio
Cumberland
County
Cumberland
County