## Slide 1
CUMBERLAND COUNTY
SCICNet
Motorola APX900
Portable Radio
Notes: Learning Event Description:
This learning event provides subscriber unit users an introduction to their unit, its basic operation, and the job aids available for assistance in operation. This is accomplished through the use of video clips, instructor facilitation, and hands-on activities whereby users are able to perform common tasks associated with unit operation.
Learning Event Objective:
Upon completion, the participant should be able to employ the toolkit resource needed to accomplish an operational task.
Learning Event Description:
This learning event provides subscriber unit users an introduction to their unit, its basic operation, and the job aids available for assistance in operation. This is accomplished through the use of video clips, instructor facilitation, and hands-on activities whereby users are able to perform common tasks associated with unit operation.
Learning Event Objective:
Upon completion, the participant should be able to employ the toolkit resource needed to accomplish an operational task.

## Slide 2: Copyrights / Disclaimer
Computer Software Copyrights The Motorola products described in this manual may include copyrighted Motorola computer programs stored in semiconductor memories or other media. Laws in the United States and other countries preserve for Motorola certain exclusive rights for copyrighted computer programs, including, but not limited to, the exclusive right to copy or reproduce in any form the copyrighted computer program. Accordingly, any copyrighted Motorola computer programs contained in the Motorola products described in this manual may not be copied, reproduced, modified, reverse-engineered, or distributed in any manner without the express written permission of Motorola. Furthermore, the purchase of Motorola products shall not be deemed to grant either directly or by implication, estoppel, or otherwise, any license under the copyrights, patents or patent applications of Motorola, except for the normal non-exclusive license to use that arises by operation of law in the sale of a product. | Documentation Copyrights No duplication or distribution of this document or any portion thereof shall take place without the express written permission of Motorola. No part of this manual may be reproduced, distributed, or transmitted in any form or by any means, electronic or mechanical, for any purpose without the express written permission of Motorola. Disclaimer The information in this document is carefully examined, and is believed to be entirely reliable. However no responsibility is assumed for inaccuracies. Furthermore, Motorola reserves the right to make changes to any products herein to improve readability, function, or design. Motorola does not assume any liability arising out of the applications or use of any product or circuit described herein; nor does it cover any license under its patent rights nor the rights of others.
APX Portable Radios

## Slide 3: Welcome
This tutorial has been prepared exclusively for you, based on your system configuration and radio layout.
It has been designed for easy comprehension, and guides you through each procedure, step by step. However, for in-depth system or radio information, you should consult your system administrator.
Keep in mind that each radio and each system is customer configurable.
APX Portable Radios
Cumberland
County
Notes: WELCOME participants to the learning event and introduce yourself.
TELL participants that this learning event takes approximately 2 to 3 hours to complete.
TELL participants that this event consists of interactive tutorials, video clips and hands-on activities.
STATE the Learning Objective for the course.
Learning Event Objective:
Upon completion of the learning event, the participant should be able to employ the toolkit resource needed to accomplish a task.

## Slide 4: Radio Overview
Cumberland
County
Soft Menu
Keys
APX Portable Radios
Channel/Mode
Select Knob
Power On/Off
Volume Control
Home
Button
4-Way Navigation
Buttons
Emergency
Button
Back Button
Top Side Button
(purple)
Push-To-Talk (PTT) Button
Middle Side
Button (1 dot)
Bottom Side
Button (2 dot)

## Slide 5: Display Indicators
APX Portable Radios
*
*
*Note: APX900 does not support encryption, WiFi, or SmartConnect.

## Slide 6: Display Indicators – cont’d.
APX Portable Radios
Note:
Battery indicator will not appear on Portables if the battery is not properly and regularly conditioned.

## Slide 7: LED Status
Cumberland
County
Solid
Conventional channel is busy
Blinking
Radio is receiving a secured transmission
YELLOW
Solid
Radio is transmitting
Double-Blinking
Radio is transmitting and emergency call
RED
Solid
Self-test being performed
Blinking
Radio is on a priority channel while in Scan List Programming mode
GREEN
APX Portable Radios
Notes: Describe the LED status, Red VS Amber and solid VS flashing.

## Slide 8: Radio Features & Menu Items
General Radio Features
and
Menu Item Functions
APX Portable Radios
Cumberland
County

## Slide 9: Radio On or Off
General Radio Features
APX Mobile Radio
E5 Control Head
APX Portable Radios
Cumberland
County
Power On/Off
Volume Control
The APX Portable radio is turned on by rotating the Power/Volume Control Knob clockwise. It will click and the radio will begin power up and self-test sequence.
The APX Portable radio is turned off by rotating the Power/Volume Control Knob counter-clockwise until it clicks.
Rotate the Volume knob clockwise to increase the volume and counterclockwise to decrease the volume.

## Slide 10: Home Mode Select
To select the home mode:
General Radio Features
Home Button
APX Mobile Radio
E5 Control Head
APX Portable Radios
Press and hold .
This will revert the radio to your pre-programmed ‘Home Channel.’ This is set as the primary dispatch talkgroup for your Home County.
Cumberland
County
Notes: This feature must be enabled by a qualified radio technician.

## Slide 11: Changing Zones or Channels
General Radio Features
APX Mobile Radio
E5 Control Head
APX Portable Radios
Cmb ZoneA Channel 1
To select a different zone, select the ‘Zone’ soft-menu button and use the “Up and Down Buttons” on the 4-Way Navigation Buttons will allow users to scroll upwards or downwards through the zone list.
ZONE
SCNL
Zone Menu Item
Zone Name
Mode Name

## Slide 12: Changing Zones or Channels
General Radio Features
APX Mobile Radio
E5 Control Head
APX Portable Radios
Cmb ZoneA Channel 1
ZONE
SCNL
Use the Channel/Mode Select Knob to change the selected mode/channel within the selected zone.
Mode Name
Zone Name
Channel/Mode
Select Knob

## Slide 13: Transmit (Trunked Modes)
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
PTT Button on Portable RSM
Lift the microphone off-hook. Press and hold the microphone PTT button.
If you hear three quick tones (callback tones) and the red XMIT (transmit) indicator lights steadily, proceed with your message.
  If you hear a busy tone and the yellow Busy indicator flashes, all trunked channels are in use.
  Release the PTT button and wait for the three quick tones. Within three seconds of hearing these tones, press and hold the PTT button to transmit your message.
  If you hear a continuous low-pitched tone, you are out of the system's range. The red XMIT indicator may flash several times as the radio tries to access the system.
Release the PTT button to receive.
PTT Button on side of Portable radio
Cmb ZoneA Channel 1
ZONE
SCNL

## Slide 14: Light/Flip
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
A short-press of the Middle Side Button will illuminate the backlight of the front display on the portable.

## Slide 15: Scan On/Off and Nuisance Delete
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
To Turn Scan On or Off:
Press the Top Side button. When scan is being enabled, the icon will appear at the top of the radio’s display. Likewise, when scan is turned off this icon will disappear.
To Temporarily Delete a Nuisance Mode:
Note:
The Selected Channel and Primary Dispatch cannot be Nuisance Deleted
Press the Bottom Side button below “NUIS” while actively scanning the talkgroup you wish to temporarily delete to no longer hear traffic from a busy talkgroup in the scan list. To restore the original scan list, do one of the following: Turn scan off, then on. Change modes. Turn off the radio, and then turn it back on.
Cmb ZoneA Channel 1
ZONE
SCNL

## Slide 16: Scan List Programming Mode
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
To Edit The Scan List:
Select the ‘SCNL’ Menu Item to enter Scan List Programming Mode.
Cmb ZoneA Channel 1
ZONE
SCNL

## Slide 17: Scan List Programming Mode
General Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Cmb ZoneA Channel 1
Sel
Rcl
Pressing ‘SEL’ will add the currently displayed channel to the scan list.
Selecting ‘RCL’ will toggle through all resources currently assigned to the scan list. These can be as you
A short press of the Home Button or Back Button will Exit the Scan List Programming mode
Notes:
Primary Dispatch cannot be Deleted from the scan list.
If a scan list is full, you will hear a bad-key chirp each time you press “SEL,” and the desired channel will not be assigned to the list. A Scan List will hold a maximum 15 talkgroups or channels.
Conventional Channels and Trunking Talkgroups cannot be scanned simultaneously.

## Slide 18: Other Menu Items
Trunked Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Use the Left or Right Buttons on the 4-Way Navigation Buttons to select more menu items:
BT – Bluetooth: Provides a list a Bluetooth status/information and Bluetooth options, such as turning Bluetooth On/Off and view currently active paired or available Bluetooth devices.
Prfl – Radio Profiles: Allows you to select one of the programmed Radio Profiles to adjust mic sensitivity, speaker settings, and backlight settings.
Left and Right Buttons
(4-Way Navigation
Buttons)
Cmb ZoneA Channel 1
BT
PRFL

## Slide 19: Emergency Alarm Activation
Trunked Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
To Initiate Emergency:
Press the Emergency button. A tone sounds and the display alternates EMERGENCY with the current zone/mode. For trunking modes, a high-pitched tone indicates that the alarm has been received by the trunked system’s central controller. 2. Radio goes into hot mic for 10 seconds, which means there is no need to press the Push-To-Talk to Transmit during this period of time. After this 10 second time period, the radio remains in emergency but a PTT will be required to relay voice communication.
Emergency Button
Cmb ZoneA Channel 1
ZONE
SCNL
This feature allows the radio to send an Emergency Beacon, which will be received by Dispatchers and other radios.

## Slide 20: Emergency Alarm Reset
Trunked Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Emergency Button
Cmb ZoneA Channel 1
ZONE
SCNL
This feature allows the radio to send an Emergency Beacon, which will be received by Dispatchers and other radios.
To Reset the Emergency:
Once a Dispatcher has confirmed emergency has been acknowledged at the Dispatch Console, press and hold the Emergency button for 3 seconds. A long steady tone sounds and EMERGENCY will no longer be indicated in display.

## Slide 21: Dynamic Regrouping
Trunked Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Notes:
System Management Function ONLY
Dynamic Regrouping allows the Dispatcher or System Administrator to temporarily reassign selected individuals, operating in separate trunked talkgroups, into a single group so they can communicate.
Being Assigned to a Dynamic Regroup:
Once the Dynamic Regroup has been initiated, navigate to
Press the PTT button to communicate to others in the Dynamic Regroup
Cmb ZoneB Dynam Regroup
ZONE
SCNL

## Slide 22: Site Trunking
Trunked Radio Features
Cmb Zone A
Channel 1
APX Portable Radios
Site Trunking is a unique Trunking mode that is considered to be an interim mode of Wide Trunking.
On a P25 system, if a site should lose all connectivity to the System Core it sends out a message indicating that it is now in “Site Trunking” mode. It will continue to send out this message until link to the Core is repaired. Radios connected to a site in Site Trunking will be able to communicate with each other locally, but calls will not be received by units affiliated at other sites.
Cmb ZoneA Site Trunking
ZONE
SCNL

## Slide 23
Cmb Zone A
Channel 1
APX Portable Radios
Examples of Agency Fleetmaps:
Cmb ZoneA Channel 1
ZONE
SCNL

## Slide 24
APX Portable Radios
Fire Police Fleetmap

## Slide 25
APX Portable Radios
Fire Police Fleetmap (cont’d)

## Slide 26
APX Portable Radios
Municipal Fleetmap

## Slide 27: Thank You for Your Participation!
ASTRO®
XTL™ 5000 Digital Mobile Radio
Model O5
Interactive End-User Training
27
:
►
◄
9
►
SCICNet
Motorola APX900
Portable Radio
Cumberland
County